## Slide 1
AIORI HACKATHON 3
HiLo-Fed
Hierarchical, Low-Rank, Drift-Triggered Federated Traffic Prediction
Communication-efficient traffic forecasting without centralizing raw sensor data
TEAM
HACKLTZS
TEAM ID
PS003 TC482
PRESENTER
Shlok Agarwal
Shlok Agarwal · shlokagarwal64@gmail.com
AIORI 3 • 14 October 2026

## Slide 2
AIORI 3
Abstract
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
2 / 11
Problem Description
Why traffic prediction needs communication-aware federated learning
1 · Privacy
Traffic sensors generate local mobility data. Raw records should remain at their source.
2 · Communication
Standard federated learning repeatedly exchanges large model updates across many rounds.
3 · Changing traffic
Rush hours, incidents and events shift local patterns; fixed schedules can waste bandwidth.
GOAL
Predict future traffic flow while keeping raw data local, reducing total communication, and preserving predictive quality close to a standard federated-learning baseline.
HiLo-Fed combines smaller updates, drift-triggered participation, and hierarchical edge aggregation.

## Slide 3
AIORI 3
Background
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
3 / 11
Background
Federated learning keeps data local—but model communication still has a cost
Federated learning
Each sensor trains locally. Only model updates are shared with an aggregator; raw traffic records stay on-device.
LoRA adapters
A low-rank adapter learns a small change to a mostly frozen model, avoiding transmission of the full model.
Concept drift
When traffic behavior differs from its recent baseline, local updates become more valuable than during stable periods.
CORE DESIGN PRINCIPLE
Spend communication where it can change the model: transmit compact updates only when local traffic has changed enough, and use nearby edge servers to reduce long-distance exchanges.

## Slide 4
AIORI 3
Literature & RFC Review
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
4 / 11
Literature & RFC Review
Relevant method families and the gap HiLo-Fed targets
Federated Averaging
A baseline for combining client model updates. Repeated full-size exchanges can be communication-heavy.
Low-rank adaptation
LoRA-style parameter-efficient updates reduce the number of trainable and transmitted parameters.
Event-triggered learning
Communication is initiated by a local change signal rather than only by a fixed timer.
HILO-FED’S INTEGRATION
• Combine update compression, adaptive participation, and edge/cloud hierarchy in one traffic-prediction workflow.
• Evaluate against standard federated averaging and a compressed federated baseline.
• Treat bytes transmitted and prediction error as joint outcomes; gains must be measured experimentally.

## Slide 5
AIORI 3
Proposed Solution
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
5 / 11
Proposed Solution
Three complementary mechanisms reduce communication without centralizing raw traffic data
01 · Low-rank updates
Freeze the shared base model. Each client trains a small LoRA adapter and sends that adapter instead of the full model.
02 · Drift trigger
Monitor local traffic behavior. Upload when change exceeds an adaptive threshold; remain quiet when conditions are stable.
03 · Hierarchical aggregation
Sensors report to nearby district/cluster edge servers. Edge servers combine updates and communicate with the cloud less often.
END-TO-END LOOP
Local traffic → local training → drift check → compact adapter upload → edge aggregation → occasional cloud aggregation → updated model returned to edge clients.

## Slide 6
AIORI 3
Solution Optimization
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
6 / 11
Solution Optimization
Baseline versus HiLo-Fed: expected design-level differences
Dimension
Conventional baseline
HiLo-Fed approach
Update payload
Full model / regular update
Small LoRA adapter
Upload timing
Fixed or frequent rounds
Triggered by local traffic drift
Network path
Clients communicate with central server
Clients → nearby edge → cloud
Raw data
Must remain local for FL
Remains local
Evaluation
Prediction error + total bytes
Prediction error + total bytes + communication tiers
Expected direction, not measured results: validate the accuracy–communication trade-off experimentally.

## Slide 7
AIORI 3
Architecture Design (UML Diagram)
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
7 / 11
Solution Architecture & Design
Hierarchical training and aggregation path
Road sensors (local traffic data)
Local model + LoRA adapter
Drift trigger (upload decision)
District edge server
Cloud aggregator
Train locally
Send only if drift
Aggregate nearby
Updated shared model / adapter state returned to edge and clients
Raw traffic records stay at sensors. The network carries compact model updates and aggregated learning—not raw traffic histories.

## Slide 8
AIORI 3
Data Flow Diagram
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
8 / 11
Data Flow Diagram
What moves, where it moves, and when
SENSOR / CLIENT
EDGE / CLUSTER
CLOUD
Traffic observations (stay local)
Train adapter + measure drift
Receive adapter when triggered
Aggregate cluster updates
Combine edge updates periodically
Global model state / updated parameters
Accounting: log payload bytes and communication frequency at client→edge and edge→cloud tiers; report total bytes alongside MAE/RMSE.
Privacy boundary: raw sensor data never leaves the client.

## Slide 9
AIORI 3
Deployment Timeline
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
9 / 11
Deployment Timeline
A practical validation sequence for the prototype
1
Baseline
Build traffic forecasting model and standard FedAvg baseline.
2
LoRA
Replace full-model updates with compact adapter updates.
3
Drift trigger
Add adaptive local change detection and event-triggered uploads.
4
Hierarchy
Introduce cluster edge aggregation and cloud synchronization.
5
Evaluate
Measure prediction error, bytes sent, rounds and tier-wise communication.
Milestones are proposed workflow steps; no performance figures are claimed yet.

## Slide 10
AIORI 3
Bibliography
HACKLTZS · A3-PS003-TC482 · AIORI Hackathon 3
10 / 11
Evaluation Plan & References
How HiLo-Fed will be assessed fairly
Prediction quality
Report MAE and RMSE on held-out traffic observations. Lower error is better.
Communication cost
Count all bytes sent, including client→edge and edge→cloud traffic.
Baselines
Compare standard FedAvg and federated learning with simple compression.
PRIMARY COMPARISON
Plot prediction error versus total bytes transmitted. The target is near-baseline accuracy with substantially fewer bytes; this remains a hypothesis until experiments are run.
METHOD REFERENCES / BACKGROUND
• McMahan et al., “Communication-Efficient Learning of Deep Networks from Decentralized Data” (FedAvg, 2017).
• Hu et al., “LoRA: Low-Rank Adaptation of Large Language Models” (parameter-efficient adaptation, 2021).

## Slide 11
Thank You
Smaller updates. Smarter timing. Closer aggregation.
Team HACKLTZS · PS003 TC482
Shlok Agarwal · shlokagarwal64@gmail.com
Questions & discussion
AIORI 3 • 14 October 2026